## Slide 1
YahBoom micro:bit creative tutorial
Lesson 19
micro:bit creative lesson 19 “Automatic door”
micro:bit entry video tutorial

## Slide 2
Part1
Learning goals
Part 2
Preparation
Part3
Handmade
Part 4
Search for blocks
Content
micro:bit entry video tutorial
YahBoom micro:bit creative tutorial
Part 5
Combine blocks

## Slide 3
Part 1
micro:bit entry video tutorial
YahBoom micro:bit creative tutorial
After you download the program,please the ultrasonic module on the side of the door. If the ultrasonic module is blocked by hand (simulating someone standing in front of the door), the servo will rotate 90 degrees to open the door. After two seconds, the door will automatically close. Let's try it together.
Learning
goals

## Slide 4
Part 2
micro:bit entry video tutorial
YahBoom micro:bit creative tutorial
Hardware:
● 1 x Micro:bit Board
● 1 x Micro:bit expansion board
● 1 x servo kit
● 1 x Ultrasonic
● 1 x door ( Owned )
● 4 x DuPont line female to male
● 3 x DuPont line male to male
● 1 x Power module
● 1 x Breadboard
● 1 x PC
● 1 x USB Cable
Then the micro:bit is connected to the computer through USB,
and the computer will pop up a U disk and click the URL in the U disk
to enter the programming interface.Input this URL
https://github.com/lzty634158/yahboom_mbit_en to get the package.
Preparation

## Slide 5
Part 3
micro:bit entry video tutorial
YahBoom micro:bit creative tutorial
handmade

## Slide 6
handmade
micro:bit entry video tutorial
Part 3
YahBoom micro:bit creative tutorial
In this lesson we will use the servos and ultrasonic module. Both VCCs must be connected to 5V.
How to distinguish the positive and negative of the servo?
The brown line of servo is the negative pole, the red line of servo is the positive pole, and the yellow line of servo is connected to P2. Ultrasonic TRIG is connected to P0, ECHO is connected to P1, and everyone can use the charging treasure to supply power to the 5v power supply module. The servo, ultrasonic and micro:bit negative (GND) must be connected to the GND of the power supply.

## Slide 7
Part 4
micro:bit entry video tutorial
YahBoom micro:bit creative tutorial
Search for
blocks

## Slide 8
micro:bit entry video tutorial
YahBoom micro:bit creative tutorial
Part 4
Search for
blocks

## Slide 9
micro:bit entry video tutorial
Part 4
Search for
blocks
YahBoom micro:bit creative tutorial

## Slide 10
micro:bit entry video tutorial
Part 4
Search for
blocks
YahBoom micro:bit creative tutorial

## Slide 11
Part 5
micro:bit entry video tutorial
YahBoom micro:bit creative tutorial
Combine
blocks
Dot matrix display distance version Dot matrix display image version
①
②

## Slide 12
Thanks for watching!
micro:bit
project
Powered by
YahBoom
micro:bit entry video tutorial
YahBoom micro:bit creative tutorial